## Slide 1: Thinkpad 701C x Framework Mechanical Guide
Karl Buchka 2/19/2024

## Slide 2: Component Overview
Bottom Case
eDP Cable Retainer
eDP Hinge Guide
Power Button
Power Button Spacer
KB-Mouse Interface Spacer
Display Panel Adapter
USB Hub Spacer (2x)

## Slide 3: Bottom Case – Permanent Hardware
M2x0.4 heat-set insert
  QTY 13
  McMaster 94180A307
2.5mm x 20mm dowel
  QTY 2
  McMaster 91585A310

## Slide 4: Bottom Case – Other Hardware
M3x25
  Keyboard (top left) and top cover fastening (Installs from bottom)
  QTY 1
  McMaster 95836A536
M1xXX
  Keyboard front edge
  QTY 4
  Original Thinkpad 701C
M2x5
  Mainboard (3x), eDP retainer (2x), indicator board (2x)
  QTY 7
  McMaster 95836A107
M2x12
  Battery
  QTY 2
  McMaster 95836A115
M2x8, low profile head
  KB-Mouse interface board (replaces existing Framework fasteners)
  QTY 3
  McMaster 93070A277
M2x10, countersunk
  Power Button
  QTY 2
  McMaster XXXXXXX
M2xXX
  USB Hub and mainboard
  QTY 2
  McMaster XXXXXXX
M2xXX
  Keyboard (top right)
  QTY 1
  McMaster XXXXXXX